## Slide 1: IoT With Arduino
Nitish Kumar Jha
GIS 2018 (Android Basic Nanodegree Track)

## Slide 2: CONTENT
What is IoT? Why we care about IoT?
How Big IoT is?
IoT in Day to Day Life and Where To Start?
Challenges/Privacy with IoT
Arduino
Overview Of Home Automation System

## Slide 3
"Think about some of the pieces of technology or up-and-coming topics that, maybe five years ago, we thought had nothing to do with us. Those of us who ignored them quickly fell behind the curve."

## Slide 4: What is IoT? Why we Care?
Internet Of People
Internet of Things : coined by Kevin Ashton in year 1999.

## Slide 5: Contt…
Refers to connectivity amongst various things and with the internet.
Things here refer to a physical object containing an embedded system(electronic circuit) within it.
Things with ability to communicate with other things or with the internet can be termed as an IOT device.

## Slide 6: Contt..
The IoT generates massive amounts of data, and cloud computing provides a pathway for that data to travel to its destination.

## Slide 7
Case 1 : beverage distribution company Diageo wanted to find a unique (and digital way) to connect sons and daughters to connect with their dads on Father's Day, the company connected 100,000 bottles of whiskey -- real, drink-filled, glass bottles -- to the internet. The reason? So that these 100,000 dads could connect to receive a personalized video message from their sons or daughters.

## Slide 8: Where To Start With IoT 1) Pay attention to the Problems available to you. 2) Anticipate the problems to Provide Solution. 3) Start brainstorming, and look for inspiration in history.

## Slide 9: Privacy / Security

## Slide 10: Arduino : Start With IoT

## Slide 11: WHY ARDUINO ??
Simplicity – easy to interface & simple coding
Robustness – turn on and off at any time, there is no shutdown of operating system
Low power consumption - easily powered
from battery
Cheaper
Suitable for electronic products

## Slide 12: ARDUINO
Microcontroller based physical computing
platform.
Does not need any OS
Need to create sketch in the arduino
language(just like C)
Inbuilt ADC.

## Slide 13: Arduino Board(s)
Is an open-source electronics platform based on easy to use hardware and software.
Typically, these boards are microcontroller boards which means that it has no OS running on top of it and will be able to run a minimalistic program.
Arduino board can be connected to a PC through USB port.
Programs a.k.a sketches are written using Arduino Language, which is merely a set of C/C++ functions.
Arduino Software(IDE): It is a text editor which can be used to write sketches and enables us to upload sketches onto the Arduino board. Arduino IDE is cross platform and can run on either Windows/Mac/Linux as it is Java based.
Arduino shields are smaller add-on boards that connect to the Arduino board to perform functions such as sensing heat, light, GPS tracking, etc..
Used if our application is core hardware centric(using sensors and actuat

## Slide 14: Topic 1: Meet Arduino Uno

## Slide 15
ARDUINO MEGA

## Slide 16
FEATURES
Microcontroller ATmega2560
Operating Voltage 5V
Input Voltage (recommended) 7-12V
Input Voltage (limits) 6-20V
Digital I/O Pins 54 (of which 15 provide PWM output)
Analog Input Pins 16

## Slide 17
DC Current per I/O Pin 40 mA
DC Current for 3.3V Pin 50 mA
Flash Memory 128 KB of which 4 KB used by bootloader
SRAM 8 KB
EEPROM 4 KB
Clock Speed 16 MHz

## Slide 18: Getting Started
Check out: http://arduino.cc/en/Guide/HomePage
  Download & install the Arduino environment (IDE) (not needed in lab)
  Connect the board to your computer via the USB cable
  If needed, install the drivers (not needed in lab)
  Launch the Arduino IDE
  Select your board
  Select your serial port
  Open the blink example
  Upload the program

## Slide 19: Arduino IDE
See: http://arduino.cc/en/Guide/Environment for more information

## Slide 20: Select Serial Port and Board

## Slide 21
todbot.com/blog/bionicarduino

## Slide 22: Some Commands
Serial.begin()
- e.g., Serial.begin(9600)
Serial.print() or Serial.println()
- e.g., Serial.print(value)
Serial.read()
Serial.available()
Serial.write()
Serial.parseInt()
Example Program

## Slide 23: Input/Output
Image from Theory and Practice of Tangible User Interfaces at UC Berkley

## Slide 24: Topic 2: Digital Input/Output
Digital IO is binary valued—it’s either on or off, 1 or 0
Internally, all microprocessors are digital, why?
1
0

## Slide 25: Arduino Digital I/0
pinMode(pin, mode)
  Sets pin to either INPUT or OUTPUT
digitalRead(pin)
  Reads HIGH or LOW from a pin
digitalWrite(pin, value)
  Writes HIGH or LOW to a pin
Electronic stuff
  Output pins can provide 40 mA of current
  Writing HIGH to an input pin installs a 20KΩ pullup
www.mikroe.com/chapters/view/1
Notes: 25

## Slide 26: Our First Program

## Slide 27: Digital IO
Use a push-button to turn ON/Off LED

## Slide 28: IO Pins
Image from Theory and Practice of Tangible User Interfaces at UC Berkley

## Slide 29: Pulse Width Modulation
Can’t use digital pins to directly supply say 2.5V, but can pulse the output on and off really fast to produce the same effect
The on-off pulsing happens so quickly, the connected output device “sees” the result as a reduction in the voltage
Image from Theory and Practice of Tangible User Interfaces at UC Berkley

## Slide 30: PMW Pins
Command: analogWrite(pin,value)
value is duty cycle: between 0 and 255
Examples:
analogWrite(9, 128)
for a 50% duty cycle
analogWrite(11, 64)
for a 25% duty cycle
Image from Theory and Practice of Tangible User Interfaces at UC Berkley

## Slide 31: Photocell

## Slide 32: WHY IoT ??
Generate, collect, process and use acquired
information to make better decisions.
Things could be anything. Physical or virtual.
Things can be interact each other smartly.
Create a social network of sensors

## Slide 33
BLOCK DIAGRAM

## Slide 34
BLOCK DIAGRAM DESCRIPTION
Transformer, rectifier and regulator is used to
provide power supply
Light is sensed by using LDR and control the
lamp through relay
Motion is detected by using PIR and security is provided by making alarm through buzzer.
Temperature & humidity can be sensed and
can be used to control fan using DHT11..

## Slide 35
Water level in tanks or even having a check on
floods can be done using ultrasonic sensor.
Plant watering is made simpler in this project by measuring moisture content on soil and watering accordingly.

## Slide 37
LDR
Used to sense light
Photocell is used
Resistance is inversely proportional to light
falling on it.
Lightly doped for required conductivity

## Slide 38: SOIL MOISTURE SENSOR
When soil having water shortage, the sensor
o/p will be high. Otherwise low.
Triple output mode. Digital o/p, analog o/p
and serial o/p
Adjustable sensitivity

## Slide 39: HCSR04
Provides 2cm-4m non contact measurement.
Module include transmitter, receiver and
control circuit.
Test distance=(high level time*velocity of sound)/2.
Plane should be smooth for accurate measuring

## Slide 40
PIR
Used for motion detection
Passive infrared sensor
3pins- gnd, vcc, o/p
o/p pin will be high when motion detected
Sensitivity 20 feet range
(

## Slide 41: DHT11
Humidity+Temperature sensor
Measurement range: 20-90%RH,0-50’C
Sends data in form of pulses train of specific
time period.

## Slide 42
ESP8266

## Slide 43
Self contained SOC with integrated TCP/IP
protocol.
1mb flash memory.
Integrated TR switch, balun, LNA, power
amplifier and matching network.
Integrated PLL, regulators, and power
management units.

## Slide 44: ADVANTAGES
Adding Convenience to your Daily Life.
Energy efficient
Customization
Ease of Use
Save Money and the Environment
Security

## Slide 45: DISADVANTAGES
Equipment and installation costs
System crashes due to any damage in the interconnection
Reliability
Difficult to control different sensors simultaneously.

## Slide 53
THANK YOU